## Slide 1: PLC 역변환기
Dualsoft.com

## Slide 2: 개요
DEV1
DEV1
LS
AB
MX
S7
File Importer
심볼리스트
로직 정보
DS
Converter
이름기준
주소기준
래더기준
POU기준
RUNG 사용기준
Json
Exporter
DEVICE
API
FLOW
DEV_N
API1(QXX.Y1)
API1(IXX.Y1)
API2(IXX.Y2)
FLOW
API2(QXX.Y2)

## Slide 3: MX

## Slide 4: Developer 버젼
0,,LDI,X40,,,,,
1,,AND,X41,,,,,
2,,AND,X4F,,,,,
3,,FROM,H4,,,,,
,,,H680,,,,,
,,,K4L5500,,,,,
,,,K2,,,,,
#P01.csv
Device,Label,Comment
M300,,MCP GOT 공정선택#205
M301,,MCP GOT 공정선택#206
M304,,MCP GOT #205 작업완료RST
M305,,MCP GOT #205 작업완료SET
M306,,MCP GOT #206 작업완료RST
M307,,MCP GOT #206 작업완료SET
COMMENT.csv
Developer.csv(EucKR)
Device,Label,Comment
M300,,MCP GOT 공정선택#DN D/L
M301,,MCP GOT 공정선택#TRV OUT
M330,,MCP GOT DN D/L 대차스토파 후진
M331,,MCP GOT DN D/L 대차스토파 전진
M332,,MCP GOT DN D/L 대차클램프 풀림
Works2.csv
BHMC3_BB_MCP1_121129
Class Label Name Data Type Constant Device Address Comment Remark | Relation with System Label | System Label Name | Attribute
VAR_GLOBAL S177_RBT3_Y_PROG_SELECT_16 BOOL Y1804 %QX6148
VAR_GLOBAL S177_RBT3_Y_PROG_SELECT_32 BOOL Y1805 %QX6149
VAR_GLOBAL S177_RBT3_Y_PROG_SELECT_64 BOOL Y1806 %QX6150
Works3.csv
"IOMaker_TestProject_Works3"
"Class" "Label Name" "Data Type" "Constant" "Initial Value" "Assign (Device/Label)" "Address" "Comment" "Comment 2" "Comment 3" "Comment 4" "Comment 5" "Japanese/日本語" "English" "Chinese Simplified/简体中文" "Korean/한국어" "Chinese Traditional/繁體中文" "Reserved1" "Reserved2" "Reserved3" "Reserved4" "Reserved5" "Reserved6" "Remark" "System Label Relation" "System Label Name" "Attribute" "Access from External Device"
"VAR_GLOBAL" "RACK_STN_TOTAL_SET_SEL" "BOOL" "" "" "M100" "" "TOTAL_SET_SEL_Comment" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "0"
"VAR_GLOBAL" "RACK_STN_TOTAL_MOD_SEL" "BOOL" "" "" "M110" "" "TOTAL_MOD_SEL_Comment" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "0"
"VAR_GLOBAL" "RACK_STN_TOTAL_QTY_CLEAR" "BOOL" "" "" "M120" "" "TOTAL_QTY_CLEAR_Comment" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "" "0"

## Slide 5: MX Work3
"P20_240109"
"PLC Information:" "QCPU (Q mode) Q13UDV"
"Step No." "Line Statement" "Instruction" "I/O(Device)" "Blank" "PI Statement" "Note"
"0" "" "LD" "L4" "" "" ""
"1" "" "OUT" "X1FA0" "" "" ""
000MAIN.csv
COMMENT.csv
"P20_240109"
"Device Name" "Comment"
"X5C" "FR:U4 Ethernet이상신호"
"X7C" "FR:U6 Ethernet이상신호"
"X0A0" "CC-LINK #1 Error"
"X0A1" "CC-LINK #1 DATA LINK"
"X0AF" "CC-LINK #1 Ready"

## Slide 6: AB
All UTF8

## Slide 7: CONV520_532.L5K
(*********************************************
Import-Export
Version := RSLogix 5000 v30.02
Owner := Windows 사용자,
Exported := Mon Aug 9 10:50:49 2021
Note: File encoded in UTF-8. Only edit file in a program
which supports UTF-8 (like Notepad, not Wordpad).
**********************************************)
IE_VER := 2.21;
CONTROLLER _CONV520 (ProcessorType := "1756-L72",
Major := 30,
TimeSlice := 20,
ShareUnusedTimeSlice := 1,
RedundancyEnabled := 0,
KeepTestEditsOnSwitchOver := 0,
DataTablePadPercentage := 50,
SecurityCode := 0,
ChangesToDetect := 16#ffff_ffff_ffff_ffff,
SFCExecutionControl := "CurrentActive",
SFCRestartPosition := "MostRecent",
SFCLastScan := "DontScan",
SerialNumber := 16#00cb_45b9,
MatchProjectToController := No,
CanUseRPIFromProducer := No,
InhibitAutomaticFirmwareUpdate := 0,
PassThroughConfiguration := EnabledWithAppend,
DownloadProjectDocumentationAndExtendedProperties := Yes,
ReportMinorOverflow := 0)
DATATYPE DateTime (Description := "Date/Time or Time Interval",
FamilyType := NoFamily)
DINT Year (Description := "Year(s)");
DINT Month (Description := "Month(s)");
DINT Day (Description := "Day(s)");
DINT Hour (Description := "Hour(s)");
DINT Minute (Description := "Minute(s)");
DINT Second (Description := "Second(s)");
DINT uSec (Description := "Microsecond(s)");
END_DATATYPE
CONTROLLER
  DATATYPE*
  MODULE*
  ADD_ON_INSTRUCTION_DEFINITION*
    PARAMETERS
    LOCAL_TAGS
    ST_ROUTINE
  TAG
  PROGRAM*
    TAG
    ROUTINE*
    CHILD_PROGRAMS
  TASK
  TREND*
  CONFIG*

## Slide 8: Siemens
*.AWL (EucKR)

## Slide 9: *.AWL
DATA_BLOCK*
  STRUCT (recursive)
  BEGIN
ORGANIZATION_BLOCK*
  VAR_TEMP
  BEGIN
  NETWORK*
END_ORGANIZATION_BLOCK
DATA_BLOCK DB 1
TITLE =
VERSION : 0.1
STRUCT
BUFF : STRUCT //Temporary
CAR_TYPE : WORD ;
C_NO : WORD ;
ROBOT : WORD ;
PROFILE : WORD ;
VIN_1 : WORD ;
VIN_2 : WORD ;
VIN_3 : WORD ;
VIN_4 : WORD ;
VIN_5 : WORD ;
VIN_6 : WORD ;
END_STRUCT ;
S171 : STRUCT //Temporary
CAR_TYPE : WORD ;
C_NO : WORD ;
ROBOT : WORD ;
PROFILE : WORD ;
VIN_1 : WORD ;
VIN_2 : WORD ;
VIN_3 : WORD ;
VIN_4 : WORD ;
VIN_5 : WORD ;
VIN_6 : WORD ;
END_STRUCT ;
https://cache.industry.siemens.com/dl/files/446/45523446/att_79269/v1/s7awl__b.pdf
Notes: try to find yours informations in the manual "STEP 7 - Statement List for S7-300 and S7-400" it is in start->simatic-> documentation-> english (language)->...
https://cache.industry.siemens.com/dl/files/446/45523446/att_79269/v1/s7awl__b.pdf

## Slide 10: *.AWL
EucKR
Parser 부적합.
  Raw text read & parse
  시작 Indent, 종료 ‘;’ 중요
  // 부터 라인 끝까지는 사용자 comment 로 해석

## Slide 11: ORGANIZATION_BLOCK
ORGANIZATION_BLOCK OB 80
TITLE = "Cycle Time Fault"
VERSION : 0.1
VAR_TEMP
OB80_EV_CLASS : BYTE ; //16#35, Event class 3, Entering event state, Internal fault event
OB80_FLT_ID : BYTE ; //16#XX, Fault identifcation code
OB80_PRIORITY : BYTE ; //Priority of OB Execution
OB80_OB_NUMBR : BYTE ; //80 (Organization block 80, OB80)
OB80_RESERVED_1 : BYTE ; //Reserved for system
OB80_RESERVED_2 : BYTE ; //Reserved for system
OB80_ERROR_INFO : WORD ; //Error information on event
OB80_ERR_EV_CLASS : BYTE ; //Class of event causing error
OB80_ERR_EV_NUM : BYTE ; //Number of event causing error
OB80_OB_PRIORITY : BYTE ; //Priority of OB causing error
OB80_OB_NUM : BYTE ; //Number of OB causing error
OB80_DATE_TIME : DATE_AND_TIME ; //Date and time OB80 started
END_VAR
BEGIN
NETWORK
TITLE =
END_ORGANIZATION_BLOCK

## Slide 12: *.SDF
“Field1”, “Filed2”, … 형태
‘,’ 구분자로 text parsing 해도 될 듯. Column 에 ‘,’ 포함하는 경우의 형태 파악 필요
"#13 T 부저정지지연 ", "T 99 ", "TIMER ", " "
"#708-1 DP1 10국이상 ","M 981.1 ","BOOL "," "
"#708-1 DP1 11국이상 ","M 981.2 ","BOOL "," "
"#708-1 DP1 12국이상 ","M 981.3 ","BOOL "," "
"#708-1 DP1 13국이상 ","M 981.4 ","BOOL "," "
"#708-1 DP1 14국이상 ","M 981.5 ","BOOL "," "
"#708-1 DP1 15국이상 ","M 981.6 ","BOOL "," "
"#708-1 DP1 16국이상 ","M 981.7 ","BOOL "," "
"#708-1 DP1 1국이상 ","M 980.0 ","BOOL "," "
"#708-1 DP1 2국이상 ","M 980.1 ","BOOL "," "
"#708-1 DP1 3국이상 ","M 980.2 ","BOOL "," "
"#708-1 DP1 4국이상 ","M 980.3 ","BOOL "," "
"#708-1 DP1 5국이상 ","M 980.4 ","BOOL "," "

## Slide 13: Resources
https://github.com/tallakt/awltool
  Ruby 기반 awl parser
Automation Workbench
https://dl.weintek.com/public/PLC_Connect_Guide/Siemens_S7_300_ET200S_Ethernet.pdf
  SIEMENS STEP 7 program allows building files of user-defined tag (*.dif file and *.AWL file), => Data Interchange Format